## Slide 1: Program IO and Interrupt
Program-controlled IO (polling)
Interrupt Driven I/O
Handling multiple devices
PIC18 Interrupt example

## Slide 2: Program IO and Interrupt
Program-controlled IO (polling)
Interrupt Driven I/O
Handling multiple devices
PIC18 Interrupt example

## Slide 3: Program-controlled IO
3
Consider a computer system
If a key is pressed,
Datain Reg contains the new key.
Status Register is set.
Notes: 3

## Slide 4: Program-controlled IO
4
Since the speed of the CPU and the speed of the human operator are different. However, we must ensure that an instruction to read character from the keyboard is executed only when a character is available in the input buffer of the keyboard interface. We must also ensure that an input character is read only once.
Consider the following Pseudocode:
WAIT_key Read STATUS
Test STATUS
if no new character, Jump WAIT_key
Read DATAIN
Notes: 4

## Slide 5: Program-controlled IO (polling)
5
WAIT_key: Read STATUS
Test STATUS
if no new character, Jump WAIT_key
Read DATAIN
In program controlled IO, the CPU repeatedly checks a status flag to achieve the required synchronization between the CPU and the input device. The programs enters a wait loop in which it repeatedly tests the device status. During this period, the CPU is not performing any useful computation.
Notes: 5

## Slide 6: Program IO and Interrupt
Program-controlled IO (polling)
Interrupt Driven I/O
Handling multiple devices
Direct Memory Access
PIC18 Interrupt example

## Slide 7: Interrupt Driven I/O
7
In many situations, other tasks can be performed while the CPU waits for an IO device to become ready. To do this, we can arrange for the IO device to alert the CPU when it is ready. It does so by sending a hardware signal called an interrupt.
The CPU allows normal program execution to be interrupted by some external signals from I/O devices.
When interrupted, it stops executing its current program and enter an interrupt sequence. The status of the current program is saved before entering the interrupt service routine (ISR) that services the interrupt.
After servicing the interrupt, the status before the interrupt is restored, execution is then returned to the interrupted program.
Notes: 7

## Slide 8: Interrupt Driven I/O
8
Notes: 8

## Slide 9: Interrupt Driven I/O
9
When an interrupt is invoked the uC runs the Interrupt Service Routine(ISR)
Interrupt vector table holds the address of ISRs
  Power-on Reset 0000h
  High priority interrupt 0008h
  Low priority interrupt 0018h
Notes: 9

## Slide 10: Steps in executing an interrupt
Upon activation of interrupt the microcontroller
  Finishes executing the current instruction
  Pushes the PC of next instruction in the stack
  Jumps to the interrupt vector table to get the address of ISR and jumps to it
  Begin executing the ISR instructions to the last instruction of ISR (RETFIE)
  Executes RETFIE
    Pops the PC from the stack
    Starts to execute from the address of that PC

## Slide 11: Program organization in MPLAB

## Slide 12: Sources of interrupts in PIC18
External hardware interrupts
  Pins RB0(INT0),RB1(INT1),RB2(INT2)
PORTB change
Timers
  Timer0 , Timer1 ,Timer2
ADC (analog to digital converter)
CCP (compare capture pulse width modulation, PWM)
... etc

## Slide 13: Enabling and disabling an interrupt
When the PIC is powered on (or resets)
  All interrupts are masked (disabled)
  The default ISR address is 0008h
    No interrupt priorities for interrupts

## Slide 14: Program IO and Interrupt
Program-controlled IO (polling)
Interrupt Driven I/O
Handling multiple devices
Direct Memory Access
PIC18 Interrupt example

## Slide 15: Handling multiple devices
15
If there are multiple interrupt lines and each of lines is corresponding to an interrupt routine. So, if INTR i is activated, the CPU will jump to the i-INTR routine. The above scheme is called as multiple interrupt line.
In many cases, several devices capable of initiating interrupts are connected to the CPU, or several interrupts use the same interrupt service routine.
Notes: 15

## Slide 16: Handling multiple devices
16
Questions:
How can the CPU recognize the device requesting an interrupt?
How can the processor obtain the starting address of the appropriate routine?
Should a device be allowed to interrupt the CPU while another interrupt is being serviced?
How should two or more simultaneous interrupt request be handled?
Notes: 16

## Slide 17: Device identification by program polling
17
When a request is received over a common INTR line, additional information is needed to identify the particular device that activated the line. The information is provided in the status in the status registers of the devices.
The interrupt-service routine begins by polling the devices (check interrupt request bit of the status registers of the devices) in some orders. The first device encountered with its IRQ bit set is the device that is serviced, and an appropriate subroutine is called to provide the requested service.
Device identification by program polling
Notes: 17

## Slide 18: Device identification by program polling
18
Polling interrupt service routine
if IRQ of device A set, jump to serve device A routine.
if IRQ of device B set, jump to serve device B routine.
::::::::::::::::::::::
::::::::::::::::::::::
Advantage : simple and easy to implement.
Disadvantage: time spent interrogating the IRQ bits of all the devices.
Notes: 18

## Slide 19: Vectored Interrupts
19
A device requesting an interrupt can identify its self by sending a special code to the CPU over the data bus.
The CPU gets the address of the corresponding interrupt service from a vector table based on the code.
The CPU will jump to the corresponding interrupt service.
NOT ALL CPUs have this mechanism.
8051 does not have
PIC18 does not have
68000 family do have
Notes: 19

## Slide 20: Priority of Interruptss
20
IO devices, or interrupts are organized in a priority structure. An interrupt request with a high priority should be accepted while the CPU is servicing another request from a low-priority device.
A real time clock interrupt should be high priority than a read key interrupt.
Priority of P18 interrupts
In PIC18, we can configure some bits in control word registers to set the priority of an interrupt.
INTERRUPT | PRIORITY
High Priority Interrupt | High
Low Priority Interrupt | Low
Notes: 20

## Slide 21: Priority of Interruptss
21
Each INTR line is assigned a different priority level.
Interrupt requests received over these lines are sent to a priority arbitration circuit in the CPU (or a external circuit).
A request is accepted only if
1. It has a higher priority than other interrupts that are being served or there is not interrupt that are being served.
2. The corresponding interrupt enable pin is enable
Notes: 21

## Slide 22: Comparison
22
QUESTION: Explain the following table
 | program IO | INT
initialize IO | CPU | IO device
overhead | small | large
speed | slow | slow
Response speed | slow | fast
Notes: 22

## Slide 23: Program IO and Interrupt
Program-controlled IO (polling)
Interrupt Driven I/O
Handling multiple devices
Direct Memory Access
PIC18 Interrupt example

## Slide 24: Sources of interrupts in PIC18
External hardware interrupts
  Pins RB0(INT0),RB1(INT1),RB2(INT2)
PORTB change
Timers
  Timer0 , Timer1 ,Timer2
ADC (analog to digital converter)
CCP (compare capture pulse width modulation, PWM)
... etc

## Slide 25: Additional Notes
  When INT occurs
  Finishes executing the current instruction
  Pushes the PC of next instruction in the stack
  Jumps to the interrupt vector table to get the address of ISR and jumps to it.
  Disable GIE (automatically)
  Begin executing the ISR instructions to the last instruction of ISR (RETFIE)
  Executes RETFIE
    Pops the PC from the stack
    Set GEIE
    Starts to execute from the address of that PC

## Slide 26: Enabling and disabling an interrupt
When the PIC is powered on (or resets)
  All interrupts are masked (disabled)
  The default ISR address is 0008h
    No interrupt priorities for interrupts

## Slide 27: Enabling and disabling an interrupt
In general, interrupt sources have three bits to control their operation. They are:
Flag bit
  to indicate that an interrupt event occurred
Enable bit
  that allows program execution to branch to the interrupt vector address when the flag bit is set
Priority bit
  to select high priority or low priority

## Slide 28: External interrupts INT0, INT1, INT2
INT (pin) | Flag bit Register | Enable bit Register | Pos or Neg Register edge
INT0 (RB0) | INT0IF INTCON | INT0IE INTCON | INTEDGE0 INTCON2
INT1 (RB1) | INT1IF INTCON3 | INT1IE INTCON3 | INTEDGE1 INTCON2
INT2 (RB2) | INT2IF INTCON3 | INT2IE INTCON3 | INTEDGE2 INTCON2
 | Set to 1 by the interrupt event. | 0 enable 1 disable | 0 falling edge 1 rising edge (default power-on

## Slide 29: Steps in enabling an interrupt
Set the GIE bit from INTCON REG
Set the IE bit for that interrupt
If the interrupt is one of the peripheral (timers 1,2 , serial,etc ) set PEIE bit from INTCON reg

## Slide 30: Example
a)
BSF INTCON,TMR0IE
BSF INTCON,INT0IE
BSF INTCON,GIE
Or
MOVLW B’10110000’
MOVWF INTCON
b)
BCF INTCON,TMR0IE
c) BCF INTCON,GIE

## Slide 31: Example
Connect a switch to INT0 and an LED to pin RB7
Every time INT0 is activated, it toggles the LED.
At the same time, data is being transferred from PORTC to PORTD.

## Slide 32: Program
ORG 0000H
GOTO MAIN
ORG 0008H
BTFSS INTCON,INT0IF
RETFIE
GOTO INT0_ISR
ORG 00100H
MAIN
BCF TRISB,7
BSF TRISB, 0
CLRF TRISD
SETF TRISC
BCF INTCON,INT0IF
BSF INTCON,INT0IE
BSF INTCON,GIE
OVER MOVFF PORTC, PORTD
BRA OVER
INT0_ISR
ORG 200H
BTG PORTB,7
BCF INTCON,INT0IF
RETFIE
END

## Slide 33: Negative Edge-triggered interrupts
ORG 0000H
GOTO MAIN
ORG 0008H
BTFSS INTCON3,INT1IF
RETFIE
GOTO INT1_ISR
ORG 00100H
MAIN
BCF TRISB,7
BSF TRISB, 1
BSF INTCON3,INT1IE
BCF INTCON3,INT1IF
BCF INTCON2,INTEDGE1
BSF INTCON,GIE
OVER MOVFF PORTC, PORTD
BRA OVER
INT1_ISR
ORG 200H
BTG PORTB,7
BCF INTCON3,INT1IF
RETFIE
END

## Slide 34: Sampling the Edge triggered interrupt
The external source must be held high for at least two instruction cycles
For XTAL 10Mhz
Instruction cycle time is 400ns,0.4us
So minimum pulse duration to detect edge triggered interrupts = 2 instruction cycle =
0.8us

## Slide 35: Example
Connect a switch to INT0 and another switch to INT1.
Every time INT0 is activated, it increments the content in location 0.
Every time INT1 is activated, it decrements the content in location 0.
At the same time, data is being transferred from PORTC to PORTD.

## Slide 36: Example
ORG 0000H
GOTO MAIN
ORG 0008H
BTFSC INTCON,INT0IF
RCALL INT0_ISR
BTFSC INTCON3,INT1IF
RCALL INT1_ISR
RETFIE
ORG 00100H
MAIN
BSF TRISB, 0
BSF TRISB, 1
CLRF TRISD
SETF TRISC
BCF INTCON,INT0IF
BSF INTCON,INT0IE
BCF INTCON2,INTEDGE0
BSF INTCON3,INT1IE
BCF INTCON3,INT1IF
BCF INTCON2,INTEDGE1
BSF INTCON,GIE
OVER MOVFF PORTC, PORTD
BRA OVER
INT0_ISR
INCF 0, F
BCF INTCON,INT0IF
RETURN
INT1_ISR
DECF 0, F
BCF INTCON3,INT1IF
RETURN
END

## Slide 37
ORG 0000H
GOTO MAIN
ORG 0008H
GOTO check
ORG 00100H
MAIN
BSF TRISB, 0
BSF TRISB, 1
CLRF TRISD
SETF TRISC
BCF INTCON,INT0IF
BSF INTCON,INT0IE
BCF INTCON2,INTEDGE0
BSF INTCON3,INT1IE
BCF INTCON3,INT1IF
BCF INTCON2,INTEDGE1
BSF INTCON,GIE
OVER MOVFF PORTC, PORTD
BRA OVER
check
BTFSC INTCON,INT0IF
RCALL INT0_ISR
BTFSC INTCON3,INT1IF
RCALL INT1_ISR
RETFIE
INT0_ISR
INCF 0, F
BCF INTCON,INT0IF
RETURN
INT1_ISR
DECF 0, F
BCF INTCON3,INT1IF
RETURN
END

## Slide 38: Example
Note that an ISR may change WREG, BSR, and Status register.
If this happens, when the CPU returns from INT, the original information may lost.
How to solve this problem?

## Slide 39: PORTB change interrupt

## Slide 40: PORTB change interrupt

## Slide 41: PORTB change interrupt
A door sensor to pin RB4 and a buzzer to pinRC7.
Every time the door is open, it sounds the buzzer by a sending a square wave for a while.

## Slide 42: Program
MYREG EQU 0x20
DELRG EQU 0x80
ORG 0000H
GOTO MAIN
ORG 0008H BTFSS INTCON,RBIF RETFIE GOTO PB_ISR
ORG 00100H
MAIN BCF TRISC,7
BSF TRISB,4
BSF INTCON,RBIE
BSF INTCON,GIE
OVER BRA OVER
PB_ISR
ORG 200H
MOVF PORTB,W MOVLW D'250'
MOVWF MYREG
BUZZ BTG PORTC,7 MOVLW D'255'
MOVWF DELRG
DELAY DECF DELRG,F
BNZ DELAY
DECF MYREG,F
BNZ BUZZ
BCF INTCON,RBIF
RETFIE
END

## Slide 43: Another Example
SW1 and SW2 to RB4 and R B5 respectively.
Activation of SW1 state change in LED

## Slide 44: Program
ORG 0000H
GOTO MAIN
ORG 0008H
BTFSS INTCON,RBIF
RETFIE
GOTO PB_ISR
ORG 0100H
MAIN BCF TRISC,4
BCF TRISC,5
BSF TRISB,4
BSF TRISB,5
BSF INTCON,RBIE
BSF INTCON,GIE
OVER BRA OVER
PB_ISR
ORG 200H
MOVFF PORTB,W
ANDLW 0x30
MOVFF W,PORTC
BCF INTCON,RBIF
RETFIE
END

## Slide 45: Outcomes
Able to describe the concept of Program-controlled IO.
Able to write a program to control a simple task based on Program-controlled IO.
Able to describe the concept of Interrupt Driven I/O
Able to describe the rationale of the steps in nterrupt Driven I/O
Able to write a program to control a simple task based of Interrupt Driven I/O
.